## Slide 1: Design and Implementation of Network Coding in NextGen Systems
Advisor:
Dr. Syed Ali Hassan
Co-Advisor:
Dr. Sajid Saleem
GROUP MEMBERS:
Shahzaib Qazi
Atif Salman Sheikh
Syed Muhammad Zain Zafar

## Slide 2: INTRODUCTION
NETWORK CODING

## Slide 3: Traditional Routing Scheme
X
Y
Y
X
Notes: Traditionally, the scheme used for forwarding data through the relay involved only decode and forward or amplify and forward mechanism, that is no complex processing was done on data reception and transmission

## Slide 4: Routing with Network Coding
X
Y
b1X + b2Y
a1X + a2Y
Notes: But as the processing power became more and more cheap, there was a possibility of doing some processing to the receiving streams at nodes before forwarding them further. Network coding refers to this possibility, because it allows us to combine incoming streams of data by performing some algebraic manipulation to them

## Slide 5: Why Network Coding?
Higher Throughput (or Data Rate)
Reduced Time Instances
Notes: Network coding allows us to achieve higher throughput or similarly reduced time instances

## Slide 6: Why Network Coding?
‘Free’ Security
x1+x2
x1+x2
x1+2x2
Send
Receive
x1+2x2
Notes: And also free security of data at the coded relays is achieved as an inherent feature.

## Slide 7
PROJECT OBJECTIVE

## Slide 8: Our Aim
Implementation of Network
Coding in MISO topologies
An Experimental Evaluation in Terms of BER and T Throughput
To code or not to Code?
Notes: The aim of our research is basically to show the feasibility of the concept of Network Coding through real time implementation on SDRs, using the experimental results to analyze the advantages and possible tradeoffs of Network Coding and to find some significant applications of Network Coding

## Slide 9
Network Topologies

## Slide 10: Two-Way Relay Channel (TWRC)
Timeslot 1 → A broadcasts X1 at frequency f1
Timeslot 2 → R broadcasts X1 at frequency f2
Timeslot 3 → B broadcasts X2 at frequency f1
Timeslot 4 → R broadcasts X2 at frequency f2
X1
X2
X2
X1
A
B
R
X1
X2
X1 ⊕ X2
Timeslot 1 → A broadcasts X1 at frequency f1
Timeslot 2 → B broadcasts X2 at frequency f1
Timeslot 3 → R broadcasts X1 + X2 at frequency f2
A
B
R
10
X1 ⊕ X2
Without Network Coding
With Network Coding

## Slide 11: Two-source MISO
X1
X2
A
B
R
C1
C2
X2
A
B
R
D
D
Timeslot 1 → A broadcasts X1
Timeslot 2 → R broadcasts X1
Timeslot 3 → B broadcasts X2
Timeslot 4 → R broadcasts X2
Timeslot 1 → A broadcasts X1
Timeslot 2 → B broadcasts X2
Timeslot 3 → R broadcasts C1 & C2 using FDM
11
Without Network Coding
With Network Coding
X1
X2
X1

## Slide 12: Three-source MISO
A
C
B
C1
C2
C3
Timeslot 1 → A broadcasts X1
Timeslot 2 → B broadcasts X2
Timeslot 3 → C broadcasts X3
Timeslot 4 → C broadcasts C1, C2 & C3 using FDM
X1
X1
X2
X2
X3
X3
B
A
C
D
R
Timeslot 1 → A broadcasts X1
Timeslot 2 → R broadcasts X1
Timeslot 3 → B broadcasts X2
Timeslot 4 → R broadcasts X2
Timeslot 5 → C broadcasts X3
Timeslot 6 → R broadcasts X3
12
X1
X2
X3
R
D
Without Network Coding
With Network Coding

## Slide 13: Theoretical Analysis
13

## Slide 14
Implementation

## Slide 15: Tools used

## Slide 16: Packet Description
Access Code
Payload
Header
Indicates start of packet/error checking
Used for conditional processing
Actual data

## Slide 17: Master-Slave Scheduling
R
B
A
Tx_start signal sent to A
Packet A sent to relay R
Tx_stop signal sent to A
Tx_start signal sent to B
Packet B sent to relay R
Tx_stop signal sent to B
Data coded in R
Coded data sent to A & B
x1+x2
X1
X2

## Slide 18: Getting Started…
Familiarization with GNU Radio Companion and Universal Software Radio Peripheral (USRP B200)
Basic Transmitter-Receiver
Basic Relay

## Slide 19
Experimental Setup

## Slide 20: Experimental Setup
Environment: Indoor, Line of Sight
Distance between successive nodes: 5m
Bit Error Rate (BER) evaluated over 2 million bits
  Total NC system TX power = total non-NC system TX power
Throughput and Goodput evaluated over 2 million bits
  Total NC system TX time = total non-NC system TX time
Results compared for NC and non-NC
A
B
R
PA+ PB+ PR = PA-NC+PB-NC+PR-NC
tTX-A+ tTX-B+ tTX-R = tTX-A-NC+ tTX-B-NC+ tTX-R-NC

## Slide 21: Two way Relay Coding (TWRC)
Source A
Relay
Source B
19

## Slide 22: Two source MISO
Source A
Relay
Destination
Source B

## Slide 23
Three source MISO
Source A
Relay
Destination
Source C
Source B

## Slide 24
Results and Discussion

## Slide 25: Non-NC schemes for all topologies
Observation:
  Minimal differences in BER characteristics
Possible explanation:
  Channel differences
  USRP calibration mismatch
  Antenna calibration mismatch

## Slide 26: Non-NC & NC schemes for 2-source topologies
Observation:
  NC curves are lower than Non-NC curves
  Percentage difference between the curves increases as transmit power is increased
Possible explanation:
  NC allows us to increase transmit power by 33%.
  Increase in Transmit powers has greater effect at higher powers

## Slide 27: Non-NC & NC schemes for 3-source topology
Observation:
  NC curves not always lower than Non-NC curves.
Possible explanation:
  Greater error due to combining of three sources.

## Slide 28: NC schemes for all topologies
Observation:
  3-source topology has greater BER than 2-source topologies.
  Minimal difference between the BER of TWRC and 2-source MISO.
Possible explanation:
  Greater error due to more number of sources.

## Slide 29: Difference between 2-source topologies
Notes: XOR-additive
LNC-multipliciative

## Slide 30: Goodput for all topologies
Observation:
  Goodput for NC schemes is greater than Non-NC schemes.
  At lower gain 2-source NC outperforms 3-source NC
  At higher gains 3-source NC outperforms 2-source NC
Possible explanation:
  NC allows to increase the transmission time
  Greater transmission time has compensated for the extra errors in 3-source NC.

## Slide 31
Simulation Results

## Slide 32: Non-NC & NC schemes for 2-source topologies

## Slide 33: Non-NC & NC schemes for 3-source topology

## Slide 34: NC schemes for all topologies

## Slide 35
2016
2017
Today
Sep
Oct
Nov
Dec
2017
Feb
Mar
Apr
May
Proposal Defence
11/10/2016
Design Expo
2/14/2017
Mid Defence
3/3/2017
Final Defence
5/19/2017
Open House
5/23/2017
32 days
9/19/2016 - 10/20/2016
Literature Review
5 days
9/19/2016 - 9/23/2016
Learning GNU Radio/USRP
7 days
9/24/2016 - 9/30/2016
Transmitter-Receiver Design
7 days
10/1/2016 - 10/7/2016
Relay Design and testing
13 days
10/8/2016 - 10/20/2016
Testing 2-Way Relay Channel
49 days
10/28/2016 - 12/15/2016
Node Designing TWRC
27 days
12/15/2016 - 1/10/2017
Relay Designing for TWRC
16 days
2/13/2017 - 2/28/2017
BER Testing of TWRC
15 days
3/3/2017 - 3/17/2017
2-source MISO and 3-source MISO topology
21 days
3/18/2017 - 4/7/2017
Testing of 2-source MISO
16 days
4/8/2017 - 4/23/2017
15 days
4/24/2017 - 5/8/2017
Quantifying results deduced
11 days
5/9/2017 - 5/23/2017
Project report preparation & Research paper submission at PIMRC
Testing of 3-source MISO

## Slide 36: THANK YOU